Haywards Heath College
Drum Light Sequencer
WJEC A Level Electronics Non-Exam Assessment Task 1

Matthias Fuller / 1-1-2022

Contents

# System Planning

## Design Brief

## Research

# Specification
- Capable of reacting to drum inputs (simulated using push to make switches)
- Capable of ‘playing’ two different light sequences
- The first sequence should turn the lights on and off sequentially
- The second sequence should flash all of the LEDs
- With no input, all of the LEDs should be off
- The surrounding hardware should only allow 20mA to flow to PIC input pins
- The system should run on 4.5V
- The unused input pins should be held low to prevent false readings

## Input Requirements
- A push-to-make switch attached to Port B.0 will trigger a set of pulses on the kick drum LED
- A push-to-make switch attached to Port B.1 will trigger a pulse on the snare drum LED
- A push-to-make switch attached to Port B.2 will trigger a pulse on the floor tom LED
- A push-to-make switch attached to Port B.3 will trigger a pulse on the high tom LED
- A push-to-make switch attached to Port A.0 will trigger the output LEDs to flash sequentially
- A push-to-make switch attached to Port A.7 will trigger an interrupt, which will lead to the output LEDs all flashing simultaneously

# System Development
## Flowchart

## Code

#picaxe 18m2

init:
bsf STATUS, RP0 ; Moves to bank 1
call initPortsB ; Initialise Port B
call initPortsA ; Initialise Port A
call initInterrupt ; Setup the interrupts
call main ; "Entry Point"

initPortsB:
movlw b'00001111' ; Sets B0-B3 to Input ; Sets B4-B7 as output
movwf TRISB
return

initPortsA:
movlw b'01000001' ; A.7 and A.0 are inputs (A.7 is interrupt)
movwf TRISA
bcf STATUS, RP0
return

initInterrupt:
W_SAVE equ B20 ; B20 should be reserved for the W_SAVE
COUNTER equ b27 ; Set the counter (i) = 0 ; Used in interrupt looping
bsf INTCON, INT0IE ; Enable external interrupt
bsf INTCON, GIE ; Enable global interrupts
return

main:
bcf STATUS, RP0 ; Move to bank 0
; Test A.0
btfsc PORTA, 0
goto serialFlash
btfsc PORTB, 0 ; If port B0
call bassPulse
btfsc PORTB, 1 ; If port B1
call snarePulse
btfsc PORTB, 2 ; If port B2
call floorTomPulse
btfsc PORTB, 3 ; If port B3
call highTomPulse
goto main
end

; Flash the LEDs
;TODO: Refactor
serialFlash:
movlw b'00000000'
movwf COUNTER

serialFlashLoop:
bsf PORTB, 4
call wait10ms
bsf PORTB, 5
call wait10ms
bcf PORTB, 4
call wait10ms
bsf PORTB, 6
call wait10ms
bcf PORTB, 5
call wait10ms
bsf PORTB, 7
call wait10ms
bcf PORTB, 6
call wait10ms
bcf PORTB, 7
call wait10ms

incf COUNTER, 1 ; increment the file register to itself
btfss COUNTER, 5 ; If the loop has iterated 16 times
goto serialFlashLoop
return

return ; Return

bassPulse: ; Pulses the bass drum 4 times
BASS_COUNTER equ b19
movlw b'00000100'
movwf BASS_COUNTER

bassPulseLoop:
; Strobe the bass drum light (PORTB.3)
bsf PORTB, 4 ; Turn it on
call wait100ms ; Wait (to produce strobe effect)
bcf PORTB, 4 ; Turn it off

; Increment the counter
incf BASS_COUNTER, 1
; Test the counter
btfss BASS_COUNTER, 3 ; Change this bit to change how many pulses
; If the counter is not done
goto bassPulseLoop
; If the counter is done
nop
return

snarePulse: ; Pulse the snare once
bsf STATUS, RP0 ; Move to bank 1
bsf PORTB, 5
call wait10ms
bcf PORTB, 5
return

floorTomPulse: ; Pulse the floor tom once
bsf STATUS, RP0 ; Move to bank 1
bsf PORTB, 6
call wait10ms
bcf PORTB, 6
return

highTomPulse: ; Pulse the high tom once
bsf STATUS, RP0 ; Move to bank 1
bsf PORTB, 7
call wait10ms
bcf PORTB, 7
return

end

resetBits:
bcf PORTB, 4
bcf PORTB, 5
bcf PORTB, 6
bcf PORTB, 7
return

interrupt: ; A.7 = external interrupt
movwf W_SAVE ; Backup working register
btfss INTCON, INT0IF ; Check the correct interrupt has occured
   ; If it did, then the next instruction will be skipped
retfie ; Return and enable Global Interrupt Register

; Reset the state of the bits
call resetBits

; Handle the interrupt
bsf STATUS, RP0 ; Move to bank 0

goto allFlash

end

; Flashes all LEDS at once
allFlash:
movlw b'00000000'
movwf COUNTER

allFlashLoop:
; Set all output bits
bsf PORTB, 4
bsf PORTB, 5
bsf PORTB, 6
bsf PORTB, 7

call wait10ms

; Clear all output bits
bcf PORTB, 4
bcf PORTB, 5
bcf PORTB, 6
bcf PORTB, 7
call wait10ms

incf COUNTER, 1 ; increment file register to itself
btfss COUNTER, 4 ; If the loop has iterated 8 times
goto allFlashLoop
return

; Ran at the end to reset the interrupt
movf W_SAVE, W ; Move the saved values back into the working register
retfie ; Return and enable Global Interrupt Register

end

Running a syntax check in Picaxe Editor 6 returns the following output:

Showing there are no syntax errors in my code, and it takes up only 20% of the maximum storage of the Picaxe 18m2’s internal storage.

## Syntax
I am new to this form of assembly language; therefore, my code had a high number of syntax errors. Most of these were fixed with a quick reference to the documentation. An example of this type of error would be specifying an incorrect number of parameters, which was particularly common when using the ‘btfss’ command. It’s easy to forget that a ‘port’ is actually an 8-bit binary number, therefore I commonly forgot to specify the bit to check. However, some errors were harder to remove. For example, control flow was falling through a return statement without the return statement invoking. This was by far the most challenging syntax error to debug. I fixed it by utilising the ‘nop’ command. This command is useless at face value; however, it proves vital in situations such as this. I didn’t realise that there must always be two lines in the same label after a ‘btfss’ command. Therefore, the ‘nop’ command was required. Another common error was when I was writing the labels to setup the GPIO pins on the PIC. This issue, predictably, was related to forgetting to change to the correct bank of registers. For example, writing to ‘PORTA’; instead of ‘TRISB’.

# System Realisation

## Testing On Breadboard
When the 6th switch is pressed, an interrupt occurs and the LEDs all flash simultaneously.
When the 5th switch is pressed, the LEDs flash in sequence.
When the other switches are pressed, their corresponding LED lights.
Concerns about button holding are not relevant because the system is designed for use with a drum kit, therefore the inputs will be pulses.

### Circuit Diagram

### Calculations
Picaxe 18m2 IC Specification
(Specification information from (PICAXE Manual, 2013))
Supply Voltage: 4.5V or 5V
Input High Voltage:
Output High Current: 20mA

Input Current
There doesn’t appear to be direct information on the Picaxe 18m2 input pin current requirements. However, given the fact most pins are bidirectional, it can be assumed that the input current is the same as the output current. Therefore, using Ohm’s Law:

With values substituted:

This value can be used for R1 in the switch voltage dividers.

Switch Voltage Dividers
The equation to calculate the output voltage of a voltage divider is shown below:

Rearranged using (Wolfram|Alpha Widgets: "Rearrange It -- rearranges given equation" - Free Mathematics Widget, n.d.):

Therefore:

# Evaluation
- Capable of reacting to drum inputs (simulated using push to make switches). Achieved
- Capable of ‘playing’ two different light sequences. Achieved
- The first sequence should turn the lights on and off sequentially. Achieved
- The second sequence should flash all of the LEDs. Achieved
- With no input, all of the LEDs should be off. Achieved
- The surrounding hardware should only allow 20mA to flow to PIC input pins. Achieved (within tolerance)
- The system should run on 4.5V. Achieved
- The unused input pins should be held low to prevent false readings. Achieved

# Improvements
Some improvements to the system may include:
- Adding a new sequence
- Adding a facility to create custom sequences. This could be done by listening for a certain input sequence, and then recording the order the switches are pressed, saving that to non-volatile persistent memory, then playing the recorded sequence when instructed to via another button on one of the unused input pins.
- Implementing the utilisation of coloured LEDs to allow for an RGB output. However, this may require a second microcontroller, or the selection of a new controller with a wider selection of pins. This is because each RGB LED is composed of a red LED, a green LED, and a blue LED. Therefore, the required number of output pins is essentially doubled.

# References

Wolframalpha.com. n.d. Wolfram|Alpha Widgets: "Rearrange It -- rearranges given equation" - Free Mathematics Widget. [online] Available at: <https://www.wolframalpha.com/widgets/view.jsp?id=4be4308d0f9d17d1da68eea39de9b2ce> [Accessed 17 May 2022].

2013. PICAXE Manual. [ebook] p.8. Available at: <https://picaxe.com/docs/picaxe_manual1.pdf> [Accessed 17 May 2022].